Modac Notes 9 Sept 2020

After upgrade in OS necessitated by use of python 3.7 (upgrade necessitated by new features in pyTK, necessitated because GLT doesn’t run on Windows 10)
And fixing of hardware i2c issues
after meltdowns (waaay over temp)

Took two SD cards and win10 laptop to Waiakoa, re-connected, and booted MODAo

reconnections: thermocouples – middle couple is wired to both the orig controller and ad16[1]
part way thru tests I disconnected it from AD16 because it was giving very irregular results.

On initial wiring up, I also hooked in the win10 laptop. I think it ran and talked with server, but later attempts (after connecting wifi) failed to connect. It wont ping 192.168.0.10 – the server IP address. Is it actually routing thru the right ethernet connection?

Ran client on the rPi along w server.
Failed to connect to ad16 and enviro – i2c failure
tracked it down to bad Differential Receiver. We may have two bad ones (one bad right from the bag!)

It ran quick simulation ok, so powered up the kiln and ran quick 100 test.

At some point AD16 suddenly started giving errors – ValueError exception from deep in the Thermocouple library – newton failed to converge or some such
created couple AD16 test functions, and test rigs in git
AD16 needed to post Voltage 0-5, not its raw values. Fixed in ad16.py. How did this ever work? Idk. But after fixing that (incl add ing ad16raw to moData and moCSV) it seemed to work correct.

(talked w Joe; then neighbor lady)

re-ran quick 100 test and it seemed to work ok… heated up, held 1m, went into cooldown.
Tried again to test the i2c and power failure modes.
Had to change program to run to 200C as the kiln was already close to 100C
with either unplugged, server would fail to start (need to put longer pause at end of script so user can see there was error?)
Unplugging during run caused different effects. Power kills only the ad16 not enviro; which didn’t quite kill the kilnProcess; apparently it was looking at kType.Status and not ad16. I added direct call to ad16.isError(), sidestepping moData (bad breaking of encapsulation, but it worked faster)

unplugging the i2c cable caused enviro to fail, throwing exception and killing the server in such a way that bypassed sending I’mDying message to clients (ooo need to set its status to that for that message!!). Fixed by re-ordering update calls from in moHardware.update() so ad16 is called before enviro.update(). Fixed 5pm

 Finally it ran ok and properly reacted to each hw failure condition; so I pulled up the slumpTest script – modified it for 1 day (1440 min) last stage (WBNI ui had a way to AddOneDay; or maybe have a preDefined CoolDown state you can add to end of script? (add coolDown btn))

modac20200909_171016. Log/ modacServerData_20200909_1710.csv
why are those fine names off? Ahhlog file includes seconds but csv does not.

Took notes on the kiln vs modac temps on phone (transcribe here later?)
seemed to be about 20-40C difference. Noting very different values on 3 thermocouples. We really only using BOTTOM [0] at present.
Slump test ran up over 600 (seen on webcam from phone while off-site) then dropped back (on next check). Came back onsite around 7pm, noting it was cooling thru 450C so shut it all down (incl kiln breaker) so it safed.

Reading log/csv file…
isnt ktype[0] supposed to be the average? Or does that get computed later?

9/14 – yes its done later.

Laptop net config:

Win10: settings> Network & Internet> Status >Change Adapter Options
opens Control Panel\Networkand Internet\Network Connections
select (dbl click) the wired Ethernet connection
select Properties
uncheck (disable) everything except IPv4
select IPv4, click Properties
select Use The following IP address:
192.168.0.2 (last digit can be any but 10 and 1; 5 is isdale desktop, 4 is isdale laptop)
subnet Mask: 255.255.255.0
no default gateway
Select Use the following DNS Server addresses
8.8.8.8 8.8.4.4
click OK and close up all.

Ping 192.168.0.10 to see if server is connected
if so, is now ok to run moTKShell client
---
9/15 after trying at Waiakoa Farmhouse
192.168.0.x is the usual for wifi and this confuses the host/ip lookup (wifi or wired?)
so changeup to use 192.16.2.x with 10 as server
that works…
WBNIf the ipaddress was a cmd line or config file item

tried to rebuild exe on morph laptop, but it fails to find some of the items installed by pip
(singleton_decorator)

Oct 8
The shutdownWhenTempDoesntRise fix is causing premature termination of the kiln. Not quite sure why. Making some changes, in new branch and working at Waiakoa

My laptop doesn’t have the required PC build environ… drat.
Ok gonna try upgrading bits there too.

On the Baumer – having Issues with getting UDP packets thru the switch.
So no updates from Baumer’s broadcast coming thru