MODAC Build Notes
Jerry Isdale, MIOAT May 2019

---------
Parts ordered per “Kiln Control Parts Rev 3.ods”, but check email to insure that is what was sent
Monday 20 May I will pick up parts from Joe Ritter at IfA and project will START
- checklist of parts
- go over first week plans

doing prelim digging on 17May
- configuring Pi: point out to some basic tutorials for setting up Pi
- multi-threading on Pi
- libraries to use for I2C and other GPIO
- python graphics tools

I need to setup work area. EShop would be best but no power and full of storage.

Bookmark and download tutorials on Particular Components
Plan Unit Tests -
1. Pi w/monitor, keyboard, mouse (then pi setup task)
  1. Which Distro? Debian? => raspian desktop w/ apps
2. Pi w/touch screen (w-audio), keyboard
  1. adafruit page has walkthru
  2. calibrate on windows
  3. touch => mouse
  4. audio output test ? No speakers bought
  5. adafruit hdmi uberguide – driver board setup
3. Pi w/wifi and bluetooth
  1. wifi only for dev => wifi works
  2. bluetooth – Leica => dont have Leica
4. I2C Ambient Environment Sensor (Temp, Humidity, Pressure)
  1. adafruit page for arduino/circuitPython, smbus?
5. I2C 24 bit AD Converter Board
  1. read what?
    1. resistor voltage divider?
    2. Thermocouple Amp Board w/thermocouples
  2. python read and report to console window
  3. python read and report in GUI
6. 8 GPIO Relay Module
  1. simple python found, bookmarked
7. 1 GPIO Power Relay w/outlets
8. I2C OLED Screen
  1. adafruit page only gives Arduino example
9. USB/TTL Serial Console Cable
  1. adafruit page windows setup
  2. python write Hello World
  3. python send all i2c AD values
  4. python send Ambient values

GPIO vs I2C
low level GPIO Zero reported good for basic io, thread mangement, servos, etc
perhaps use it for Relays?
Adafruit says use their CircuitPython API (adafruit_blinka) for I2C
SMBus/SMBus2 or PigPi or ?? for Python I2C and GPIO?

Define Pin Usage:
- which I2C or both?
- Where are relays (9 gpio)?
21May2019
picked up parts from Joe yesterday. They ordered several extra of some things. I kept to the list, see spreadsheet. No power or hdmi cable provided so borrowed a D-plug power cable from other parts (one of the ac/dc control relay boxes I think). Using a MIOAT provided keyboard and hdmi cable.

Setup per https://www.raspberrypi.org/documentation/installation/installing-images/mac.md
Start by downloading Raspbian Stretch with desktop and recommended software from
https://www.raspberrypi.org/downloads/raspbian/
2019-04-08-raspbian-stretch-full (in Mac’s project RPi3BPlus)
SD Card is 32GB formatted FAT-32, is read only on mac initially
https://www.youtube.com/watch?v=nehn7mh81vs part way tween open/locked
move into IFA Kiln Controller/RPi3BPlus and unzip
Unmount using diskUtil
then run dd copy to install
sudo dd bs=1m if=2019-04-08-raspbian-stretch-full.img of=/dev/rdisk2 conv=syn
hmm took several tries and had to use disk2s1 and
it doesent boot… wtf. Old pi w/card works on other monitor.
Try BalenaEtcher https://www.balena.io/etcher/
Ok that worked, with IfA monitor, moca mouse and my keyboard
boots to desktop, setup location,
pi user change pwd: modac
screen size (black box not visible)
setup wifi access -
update software – hmm an error about hashes
reboot

Unit Test 1 COMPLETE – pi boots with monitor/mouse/keyboard

open console
try PyQT5 tutorial https://build-system.fman.io/pyqt5-tutorial
python3 -m venv venv
source venv/bin/activate
pip install PyQt5 --- could not find a version that satisfies the requirement PyQt5

do we have net? Try speedof.me … 8.36Mbps down, 6.97Mbps up,
Back on mac, try pyqt tutorial, needs py3 first
 https://docs.python-guide.org/starting/install3/osx/

back on Linux, run the apt-get updates…
1. `sudo apt-get update`
2. `sudo apt-get upgrade` (Choose `Y` when prompted)
3. `sudo shutdown -r now`
after reboot
4 `sudo raspi-config`
enable I2C, expand filesystem
and done… so far.
Back again and try install PyQt5
from https://raspberrypi.stackexchange.com/questions/87125/installing-pyqt5-on-raspberry-unable-to-imoprt-pyqt5-sip/87129
rpi ~$ sudo apt install python3-pyqt5

$ pip install --user pipenv

22 May

NOTE: will need to do proper py3+pyqt5 install on windows machine, perhaps an Installer per gui tutorial?
NOTE: use pip3 for python3

plan out what needs installing for unit tests
- Py3
- PiEnv ? Allows multiple py environments
- GUI
  - PyQT5
  - QT Creator https://www.qt.io/download
  - pyqtgraph pip3 install pyqtgraph
- TouchDisplay
  - https://www.adafruit.com/product/2397
  - https://learn.adafruit.com/hdmi-uberguide/2397-7-touch-display-1024x600-w-slash-audio
  - https://learn.adafruit.com/hdmi-uberguide/rtd2668-hdmi-vga-ntsc-pal-driver-board-audio
- gpioZero? https://gpiozero.readthedocs.io/en/stable/
  - relay – generic DigitalOutputDevice
    - https://gpiozero.readthedocs.io/en/stable/api_output.html
    - https://tutorials-raspberrypi.com/raspberry-pi-control-relay-switch-via-gpio/
    - GPIO vs gpioZero – former is low level, latter has nice event methods
- I2C
  - CircuitPython vs SMBus2 vs ?
    - Use SMBus2
    - https://www.pololu.com/docs/0J73/15.9
    - https://github.com/kplindegaard/smbus2
    - pip3 install smbus2
  - Rpi.org “Programming an i2C interface in Python”
    - mentions PiGPIO C++ lib/daemon w/Python interface
      - http://abyz.me.uk/rpi/pigpio/
      - https://github.com/joan2937/pigpio
      - looks very interesting for our use. A daemon (w/security) can be controlled over socket/pipe from PC or local Python interface
    - https://www.raspberrypi.org/forums/viewtopic.php?t=173781
  - BME Environ Sensor :
    - https://pypi.org/project/RPi.bme280/
    - use RMHull BME280 over smbus2
      - https://github.com/rm-hull/bme280
  - A/D converter
- Console Cable: https://learn.adafruit.com/adafruits-raspberry-pi-lesson-5-using-a-console-cable/software-installation-windows

Software Components
Trade offs and selection of methods for unit test and integrated MODAC
1. GUI: python, linux/windows, graphing + buttons, menus
  1. QT, w pyqtgraph
  2. matplotlib https://matplotlib.org/ (Qt, GTK+, TKinter)
  3. guizero
  4. gtk/PyGObject
  - pyqtgraph is faster. Stick w it
  - but commercial license VERY expensive ($500.mo)
  - matplotlib works
I2C control
  - smbus2 https://github.com/kplindegaard/smbus2
  1. circuitPython (prefer not)
  2. Pigpio - https://github.com/joan2937/pigpio http://abyz.me.uk/rpi/pigpio/
    1. runs as daemon, might be easier for network connection
    2. http://abyz.me.uk/rpi/pigpio/python.html
  3. Devices
    1. BME sensor,
    2. OLED screen
    3. A/D converter,
2. Relay Control
  1. gpio
  2. gpioZero https://gpiozero.readthedocs.io/en/stable/installing.html
  3. circuitPython No.
  - https://www.makeuseof.com/tag/gpio-zero-raspberry-pi/ => gpioZero
    1. https://www.raspberrypi.org/forums/viewtopic.php?t=204466
    2. use LED class to run relays?
2. Comm/Network – message passing?
  1. Serial comm over USB
  2. Ethernet
3. Timed Events (PID control)
4. PID calculations – multiple sensors/heaters

Order of tests…
Basic setup w/keyboard-mouse-monitor (DONE)
Proper Python environment incl editor/IDE
simple GUI apps? (QT and pyqtgraph tutorials)
I2C on BME sensor
Relays
AD Converter w test loads
OLED Screen
touch display
comm/network & PC setup

25May
think I mucked up the system trying to install Ninja-IDE… it may be included with distribution
so go back to Initialize SDCard with BalenaEtcher
(keep img zip around but toss the img file when not using it)
GUI Boots
> Setup Location.
> Setup WiFi
>Update Software
(screen saver kicks in, move mouse)
> restart after update

back on Linux, run the apt-get updates…
1. `sudo apt-get update`
2. `sudo apt-get upgrade` (Choose `Y` when prompted)
3. `sudo shutdown -r now`
after reboot
4 `sudo raspi-config`
enable I2C, expand filesystem

now test out Python3 and IDEs
Ninja-IDE isnt showing up, so go with other for now
work thru BaldEngineer tutorials-raspberrypi.com
https://www.baldengineer.com/raspberry-pi-gui-tutorial.html
… asks to install QT Creator by downloading from QT site, which gives a 30 day trial license and option for commercial license
annoyingly the .run files are not proper format
apparently need to download and rebuild locally from source!
?? Hopefully MO/IfA will go with QT but may be too expensive, so need to consider MatPlotLab

sudo apt-get install qt-5default
sudo apt-get install qtcreator

enter qtcreator on cmd line and it starts!
Sorta no examples apparently
bah.
Since may not use it now, go on to other GUI test

PIGPIO – follow method 1 install http://abyz.me.uk/rpi/pigpio/download.html

matplotlib – sudo python3 -m pip install -U matplotlib
testing matplotlib basic_example.py … opens wth Thonny IDE
and two graphs start plotting … great
ok did a couple graphs etc with matplotlib and its fine.
Will need to investigate more

NEXT! … i2c with BME
following https://pypi.org/project/RPi.bme280/
with help on pins from https://learn.adafruit.com/adafruit-bme280-humidity-barometric-pressure-temperature-sensor-breakout/python-circuitpython-test

i2c tools already installed.

sudo pip3 install Rpi.bme280

i2cdetect -y 1
shows nothing on the bus?!
No data. Test program also gives zilch.
Is board ok? Is pi ok?

26May ---
brought over some other i2c devices (displays) and a teensy on breadboard setup to run an Adafruit 8x8 matrix
Pi3 doesnt see BME280
teensy sees large 8x8matrix as #70
pi1 sees it there too
pi3 also sees it

small 8x8 was working, may have fried w/mis-wired power
test BME280 again on Pi3, then pi1, chain on i2c with led matrix
SEES BOTH!!! yeah!!

can now do BME Python tests
https://pypi.org/project/RPi.bme280/
WORKS!!

28May
found strip chart in matplotlib, should be able to mod it to show BME values

Dig into ADConverter LTC2499 … Analog Devices eval board we have has its own multi-pin connector to either their Linduino or to a USB eval board. It also exposes the I2C and power pins directly for the LTC2499 device. EEPROM on board is on separate I2C bus accessible thru big connector or perhaps some TestPoint pins.
Wire wrap/solder points are attached around the perimeter of the board for Power/Gnd/AnalogChan. Two thru hole points for I2C.
Will need to add an I2C wire: JST 4wire connector?

A.Dev Linduino is their custom Arduino compatible designed for testing their boards. Aside from usual Arduino connectors, it has the multipin connector (https://www.analog.com/en/design-center/evaluation-hardware-and-software/linduino.html)
They provide a software library LTSketchbook (.zip on that link) to control the board and its various daughter cards.
I downloaded it into the ADConverter folder and extracted the relevant files.
While they are for that particular arduino variant, they look helpful in dealing with details of the board.
This board is going to take some serious spelunking to understand and control properly.

Directions next? Either play with GUI for BME or move on to other boards
Relay boards would be easy next step. May need to create some dummy loads but simply setting them using different GPIO libraries would be sufficient.
And.Or try some PiGPIO examples for the C daemon use of I2C and gpio
pigpio has nice looking thread interface too.
Not sure if there is need for security on this…. I could break my rule and ignore security for now (design in security FromTheStart)

Found some good resources on AD Converter
https://www.raspberrypi.org/forums/viewtopic.php?t=64503
https://www.iascaled.com/store/ARD-LTC2499-LIB
https://raspberrypi.stackexchange.com/questions/69116/a-d-converter-solution
https://www.raspberrypi.org/forums/viewtopic.php?t=64503

Most encouraging is the IAScaled Arduino board with the LTC2499 ADConverter which comes with a C++ library to run it. Could be translated
Discouraging is a note that the board or other references in above links uses 5vdc and level shifting is needed for 3.3v pi
however another of the above links shows a board using 3.3v
https://www.raspberrypi.org/forums/viewtopic.php?t=64503
Looks to be a repurposed version of the demo board complete with the EEPROM but in a Pi HAT form factor (slightly smaller.
Note it is a 2013 era and uses the smaller 26pin PI from v1, not the 40pin Pi3B
Scrolling down it also includes code for QuickWire interface which is 6yrs out of date
https://github.com/quick2wire/quick2wire-python-api

29May

Simple GPIO test on GPIO-21 to blink light on the controlled power strip s-com
from https://electronicshobbyists.com/raspberry-pi-gpio-control-led-blinking-with-raspberry-pi/

and with gpio zero…
https://gpiozero.readthedocs.io/en/stable/
trivial!!!

so to do the 8 relay block, need 8 signal wires, gnd, and relay power (5v), plus something on the otherside of relay

PI EZConnect is not really that easy to connect and layout needs to be carefully checked.
Redo the BME280 using EZConnect – so easier to connect up the other devices… although I2C is going to be interesting
i2c devices: bme280, ad, oled
EZConnect offers 3 tie points for the i2c – screw terminal and two solder points.
Suggest setting up JST 4 wire on each… gives 3 modular attach points for i2c

OLED Library in Python for Pi https://github.com/adafruit/Adafruit_Python_SSD1306
adafruit one uses circuitPython which we may avoid
Luma https://github.com/rm-hull/luma.oled
https://pypi.org/project/ssd1306/ (links to luma. Ssd is old version)
Note any of these works on some i2c comms. Luma ones have own code
https://github.com/rm-hull/luma.core
seems to be based on smbus2
https://github.com/rm-hull/luma.core/blob/master/luma/core/interface/serial.py
https://github.com/rm-hull/luma.examples
30 May

EZ Connect works with I2C
Moved test programs to MODAC_Tests

wired 3 female JST SM onto I2C lines of EZConnect board
tested all 3 against the BME280.

BME280 is Device id 77 per i2cdetect -y 1

Hmm OLED is not seen. Re-read docs.
Ok… DATA => SDA SA0 is NOT SDA. Now it works and OLED is id 3d
trying tutorial https://www.raspberrypi-spy.co.uk/2018/04/i2c-oled-display-module-with-raspberry-pi/
which uses the Adafruit library https://github.com/adafruit/Adafruit_Python_SSD1306
and I get a Snowcrash.
Posted query to Adafruit forum https://forums.adafruit.com/viewtopic.php?f=50&t=152398

31May

AD converter wired in too. Shows up as i2c 0x77 which matches docs on default jumpers.

Next up – wiring the thermocouple amplifier and solenoid boards.
Amp board has +5v and ground, and 4 +- lines for each channel. ADC has tie posts for + and common ground line.
Do the signal wires/lines after amps need to be special wires?
 2Wire mini JST pairs might be good for the amp-ad connection, or direct wire? Connectors first.
Or perhaps a 5 or 6 wire JST with one or two grounds? Need to read up on amp/ad connections

Relay board is simpler. Example from Poofer. Vcc line could be 5+ or maybe 3v?
8+Vcc+Gnd connections – simple 10 pin out? Setup a rail with 5v feed (amp + relay)
can vcc be 3.3 or just relay control? Need read up again.
Pi control lines are 3v (maybe 5v tolerant?)

Need common Ground bus at least.
Perhaps one for 5v from power supply and another 3.3v?

--- 3June
relay board wired in, moved controlled outlet gpio

Wiring is becoming a priority … component layout and wire routing.
2 x regular i2C (bme280, adconverter)
1 x i2C + one GPIO (oled)
8 line + 3v, 5v, 2xgnd relay

need to learn how to format datetime timestamp for printing

How to test the ADConverter?
Thermocouple amps + thermocouples (3)
bend resistors?
Do we need to show all 8, 16 channels running?

Also get GitHub repository started for unit tests

relays: active Low, so using gpioZero we can set up OutputDevice( …, active_high=False)
or do it in hardware with some sort of Inverter gate (3v? Bipolar highV?)
as in this blog http://baskauf.blogspot.com/2018/02/turning-stuff-on-and-off-using.html

swapping out the 5vdc USB power supply for larger 10A one.
Need USB-micro cable end to connect to 5vdc bus and ground
Pin Out http://www.hobbytronics.co.uk/usb-connector-pinout

--- 4June
- GitHub linux – either learn cmd line or find tool (ugh got local repo working but wont upload)
- find USB cable to ‘customize’ DONE
- wire up thermocouple amps & devices to ADConverter
- test converter software… need to write Python library for this (IowaScaled Arduino lib example)
- setup touch-display & test
- Layout demo setup on board (new wires)

ADConverter – looks like I need to write the python library
IowaScaled C++ gives details for the LTC2499 chip
Adafruit has 2 Python libraries (one old, new is CircuitPython)
neiter of those support the LTC2499 so at best they are library API examples

TouchDisplay: https://www.adafruit.com/product/2397
well that was trivial. Plug in hdmi, find a USB mini cable (for touch usb interface) and make a power line (from 5v bus blocks to barrel connector)
Fire up the Pi and it works.
Too small and fragile for development but cool.
Adafruit recommends their Wire Stand for it https://www.adafruit.com/product/1679 (out of stock)

6 June

Other file started to look at the Python code needed for AD Converter

Probably need to put an i2c compatible level shifter in to the mix for AD Converter.
I should have one of these 4 bit Adafruit ones somewhere (ordered in 2012) https://www.adafruit.com/product/757
Speed cant be cranked up but that should be ok. We are not needing fast updates
Also I have a 4 bit level shifter from Sparkfun

The SF I2C tutorial is very good… https://learn.sparkfun.com/tutorials/i2c/all
Fortunately we dont need to really know all the wave forms of the i2c bus… but might be fun to watch em

Initial test: use resistor switch box and potentiometer with 3.3v – Gnd spread. May need to link COM→GND and REF +- to GND/3.3v too.
Use this as the initial hardware and get on with the software.
Later we will try with level shifter, 5v and thermocouple+amp

12 June
AD Board is recognized by i2cdetect, but not found in basic python tests (using slightly modified code from the forum post code on the AD HAT
https://www.raspberrypi.org/forums/viewtopic.php?f=37&t=64503
more notes going into “LTC2499 Python Support Design Doc.odt”

fall back testing… trying board on Teensy 3.2.
first test: BME280 testing to prove I2C runs… pins on the JST connector were loose, fixed and then ran Adafruit BME280Test	installed two libraries into Arduino IDE per the Adafruit tutorial
https://learn.adafruit.com/adafruit-bme280-humidity-barometric-pressure-temperature-sensor-breakout

Next try the ARD-LTC2499 arduino library (ard2499_test) even though we dont have EEProm
need to copy/install library (documents/arduino/libraries)
comment back in “goto SkipJumpers” at top of loop()
hmm prints long line of ‘-’ maybe not finding board?
That print comes from the Read

Digging around I found IowaScaled makes a 3.3v version of their arduino board https://www.iascaled.com/store/ARD-LTC2499-3V3
as the ARD-LTC2499 page says
https://www.iascaled.com/store/ARD-LTC2499
Note: The normal ARD-LTC2499 is not compatible with Arduinos using 3.3V I/O on the I2C lines, such as the Due, Zero, etc. This is because the LTC2499 requires a 5V supply to deal with the 4.096V reference voltage, making it incompatible with 3.3V I2C. A 3.3V compatible version is available here.
https://www.iascaled.com/store/ARD-LTC2499-3V3

So best to get the 5v level shifter setup running
will examine the schematics of their 3.3v board
---
17 June.
Arduino test of board returns NAK
ADS1115 16bin AD i2c boards arrived, along with level shifters, etc
so switch over to getting those w/thermocouple amps running

started Notes file in ADS115 folder, leaving off the LTC2499 Notes for now

Found my QWIIC cables and boards. These let you daisy chain i2c boards and offer a cleaner wiring setup than the large JST single point ones
Two JST connections on Rpi can feed two directions of i2c sensors, making for easier layout
but may need more breakout boards… (4 on hand)

plan:
1. wire up ads1115 to read 5v driven thermocouple amps & thermocouples
  1. first get ads 1115 reply on i2c and perhaps read 1 pot 5vdc or 3vdc
  2. then wire in thermocouple amp and t’s
2. GUI: plotting BME280 in several GUI with numeric reads and buttons
3. PC Comm Test: unit test for serial console cable, ethernet, usb
4. Layout demo setup
5. define demo apps

18 June
oops, may have fried Pi with misconnected Qwiic board
got replacement from Joe (ordered 2x from amazon)
boots ok but requires my 8gb usb stick installed or it gives error… need to permanently unmount

19 June
graphing in MatPlotLab with ADS1115 working … chan 0 is potentiometer, chan 1 is wired to thermocouple via the amp board
note that voltages from the ampboard are still VERY low, so use the on board amp of ADS1115 at gain factor 8
(translates to ???)
what is the mapping of raw→volts→temp? Heating with hot air gun looks like it can max out the sensor, at least at that gain
Note that gain needs to be set for each channel before read or all channels use came gain.
May need to adjust gain depending on the temp range being monitored.
Noting the red/yellow wires on thermocouple do matter. Red in Negative, Yellow in Positive gives a curve UP as temp increases
reversed quickly drove to 0 with heat gun

looking for alternative ways to access AD and i2c, as the Adafruit circuitPython stuff hides heavily and doesnt support LTC2499.
Also ordered a different py shield AD+DA board

Looking into PyQT interfaces
first install PyQT
apt-get install qt5-default
sudo apt-get install python3-pyqt5
 (says its there)
build simple window per:
https://pythonspot.com/pyqt5-window/
works fine.
Now try VisPy for mandelbrot
sudo pip install vispy
hmm mandlebrot says I still need something to run
ahh pyqt5/pyside2
nope.
Vispy says use pyqt4
vispy.org/raspberry.html

–
20June
trying to build a python i2cdetect … found code online that sorta works, although it uses Variable Annotation, which was added in Python 3.6
our Python is v3.5… so try updating to 3.7.0 (per dec 2018 instructions https://installvirtual.com/install-python-3-7-on-raspberry-pi/
or https://www.alauda.ro/2019/01/how-to-install-python-3-7-on-raspberry-pi/

well that messed things up.
Time to rebuild from start
Setup per https://www.raspberrypi.org/documentation/installation/installing-images/mac.md
2019-04-08-raspbian-stretch-full (in Mac’s project RPi3BPlus)
Using BalenaEtcher (in Applications) select that image, the sd card and Flash!
(be aware of SD card locking on mac issue)
put in Pi, boot, set location, language, date, net, etc.

1. `sudo apt-get update`
2. `sudo apt-get upgrade` (Choose `Y` when prompted)
3. `sudo shutdown -r now`
after reboot
4 `sudo raspi-config`
turn on i2c, expand filesystem
reboot

now try getting py7 again

from: https://www.ramoonus.nl/2018/06/30/installing-python-3-7-on-raspberry-pi/ get this line:
sudo apt-get install -y build-essential tk-dev libncurses5-dev libncursesw5-dev libreadline6-dev libdb5.3-dev libgdbm-dev libsqlite3-dev libssl-dev libbz2-dev libexpat1-dev liblzma-dev zlib1g-dev libffi-dev
From https://dastoev.com/posts/2019/03/install-python-3-7-on-raspberry-pi/ get latest python
wget https://www.python.org/ftp/python/3.7.3/Python-3.7.3.tgz
tar xf Python-3.7.3.tar.xz
cd Python-3.7.3
./configure –enable-optimizations
make
sudo make altinstall

Note this build takes a LOOONG time. Dont ever do the ‘-enable-optimizations’ again!!
maybe copy sd card when this is done

make it default python3 (where did it go?)
created lnkPython.sh to unlink and ln -s the various main programs that were pointing at py3.5
https://stackoverflow.com/questions/44967202/pip-is-showing-error-lsb-release-a-returned-non-zero-exit-status-1/56699756#56699756’
had to fix usr/bin/lsb-release to point at python3.5 directly (not python3 which is now 3.7.3)
Test
python3 -V

now start bringing in the apps & libraries

sudo apt-get install qt-5default #failed to find this
sudo apt-get install qtcreator
sudo apt-get install i2c-tools
sudo apt install python3-gpiozero
sudo apt-get install rpi.gpio
sudo apt-getinstall python3-pyqt5
sudo python3 -m pip3 install --upgrade pip setuptools wheel
sudo python3 -m pip3 install -U matplotlib
sudo pip3 install pyqtgraph
sudo pip3 install smbus2
sudo pip3 install adafruit-blinka
sudo pip3 install adafruit-circuitpython-bme280
sudo pip3 install Rpi.bme280
sudo pip3 install Adafruit-SSD1306

matplotlib fails – error about multiarray numpy
grrrr.
21June Solstice
Much futzing and googling
made unlinkPython to set back to python.35 but I think I lost pip3
   sudo apt-get uninstall numpy
and then run getModac seems to be collecting… at least it hasnt blown up w. long error message about numpy
yet
ok it completed all installs
but now Thonny IDE doesnt start from Applications>Programming list!
Sudo pip3 install thonny

shoots… still having ‘Issues’
found similar issue report on numpy github and filed comment:
see https://github.com/numpy/numpy/issues/13238?_pjax=%23js-repo-pjax-container
saved errors into several files on pi/*
copied those and the .sh to 8Gb usb drive and copied those to mac $PROJECT/RPi3BPlus/pi-home
create a 2nd Sdcard (1 black stripe), flash with raspian
try it with basic system
ok so something in my loads is mucking up the numpy/multiarry stuff.
Gonna try again with fewer loads at start

so do the basic apt-get update, upgrade
dont get qt5 stuff or pyqtgraph
or matplotlib first time
all seems to work ok.
Do single line for matplotlib
install seems to have worked
add oled support line
and that is working too.
Ok lost 2 days but its back to functional.
---
24 June
plan:
make qwiic connector to JST
also qwiic 2 level shifter to LTC2499
test ltc2499 board temp read/response
to confirm if board is non-responsive
then work on graphing UI

vendor responded asking for scope traces of i2c comms to ltc2499.
Better to use arduino mega for this perhaps.
Modified the ARD2499 to emit serial verbosely at low level

Or perhaps copy the full Ard2499::ltc2499ReadTemperatureDeciK() into Basic_hello
–
WaveShare AD Board from amazon provides alternative AD (and DA) conversion in a HAT format.
It uses SPI so need to be sure our use for other parts (relays in particular) does not interfere
Here are the pin interfaces from https://www.waveshare.com/wiki/High-Precision_AD/DA_Board#Interface_Definition
Note these are PINS not GPIO, so need to translate them
Pin	Symbol	Description
1, 17	3.3V	Power supply (3.3V)
2, 4	5V	Power supply (5V)
3, 5, 7, 8, 10, 18, 22, 24, 26, 27, 28, 29, 32, 36, 38, 40	NC	NC
6, 9, 14, 20, 25, 30, 34, 39	GND	Ground
11	DRDY	ADS1256 data ready output, low active
12	RESET	ADS1256 reset input
13	PDWN	ADS1256 sync/power off input, low active
15	CS0	ADS1256 chip select, low active
16	CS1	DAC8532 chip select, low active
19	DIN	SPI data input
21	DOUT	SPI data output
23	SCK	SPI clock
31, 33, 35, 37	GPIO	extend to sensor interface

From relayModuleTest.py
relay1 = OutputDevice(21,active_high=False)
relay2 = OutputDevice(20,active_high=False)
relay3 = OutputDevice(16,active_high=False)
relay4 = OutputDevice(12,active_high=False)
relay5 = OutputDevice(7,active_high=False)
relay6 = OutputDevice(8,active_high=False)
relay7 = OutputDevice(25,active_high=False)
relay8 = OutputDevice(24,active_high=False)

so using GPIO 7, 8, 12, 16,20,21,24,25 … no conflicts!!
but only 2 gpio left
use GPIO4 (or 5) for OLED reset
nope forgot the power strip.. that was on 36.
move it to 5 and oled on 4 and we have no pins left.
–

Documented pins in MODAC Pi Pins sheet of Pin Usage.ods
Adding WaveShare board means turning on SPI…
so add this to setup
1. raspi-config > Interface > turn on SPI
2. sudo pip3 install spidev

Then run the WaveShare AD-DA test… it reads!!
AD0 = on board POT
AD1 = on board Photoresistor
AD2 = my potentiometer
AD7 = thermocouple
all show signs of changing

great I like this board MUCH better than the LHC2499 at least for its physical connections
and lack of need for level shifter

revising Waveshare’s python code for use as a package
adding functions to read lower/upper 4 with gain
so lower is at gain 0 (0-5v pots&photoresistor)
and upper can be thermocouples with higher gain
gain values to chip are 0,1,2,3,4 which are x1, x2,x4, x8, x16, x32
waveshare has dict with string lookup, I added one that converts 1-32 into nearest proper value

ok it works, in waveshareTest2 – ignore the convertTemp() as it is wrong
using a cup of ice water > heat gun and gain=1 get 0.2v->3.8v
do a git push
use command line stuff w/account morphoptic pwd (substitute one 0)

two sd cards now switch between em.
One card (black marked) has the UnitTestDemo folder of python apps for step 1 demo
Still need:
- GUI w/chart+numbers+buttons
  - matplotlib + GTK
  - pyqtgraph + QT4 (latest for windows+linux)
    - qt5 is only android and linux at present
- Remote Display/Control
  - console serial co­mm w/windows machine
  - ­ethernet comm with windows machine

GTK gui: http://blog.borovsak.si/2009/09/glade3-tutorial-1-introduction.html

Should we try mixing data yet?
BME280 + ad (4 traces)
T, H, P, t0, t1, t2, pot1, pRes, p2
RT data flow not in above gui tutorial – how to get clock interrupt in GTK
Glib.timeout_add https://www.gtk.org/tutorial1.2/gtk_tut-17.html

GtkWindow
- timeout or Idle (to update from data, maybe socket)
- GtkVBox
  - GtkMenuBar (basic menus?)
  - GtkToolBar (more icon/buttons)
  - GtkHbox
    - GtkScrolledWindow
      - GtkTreeView (data list)
    - GtkGrid 3x3?
      - GtkVbox (graphs)
  - GtkStatusBar

ok not too happy with that tutorial as it doesnt match Glade interface
newer glade (3.22) in git.gnome but not built for Raspian so ignore for now

Consider insead simple gui:
GtkWindow
- Idle or timeout to collect data
- GtkVbox
  - GtkHeaderBar (title, menu, tool)
  - GtkHbox ?
      - matplotlib graph of 1 analog
      - text box of latest value
  - GtkHbox ?
    - Scroll window w cells of data
  - GtkStatusBar (for msgs)

NOTE: Thonny (python ide) sometimes loses its menu bar.
https://www.kirkmakse.com/raspberry-pi-raspbian-missing-menu-bar/
fix is to remove ~/.config/lxpanel
then restart the app or whole machine

working thru gtkMatPlot_sheet1 to make a spreadsheet of BME data
and a plot of one or more columns

might look at https://developer.gnome.org/pygtk/stable/class-gtktreeview.html#method-gtktreeview--insert-column-with-data-func

its getting there… doesnt compile yet.
ListStore needs way to define columns properly
odd there isnt a good listStore backed by column data (as from db) that easily loads row from numpy array backing MatPlotLib.

3July
gtkMatPlot_sheet1 working well.
Look into how to convert to customTreeModel to hold data better.
Thats a start on custom data model that will collect all MODAC data and make it available for display, save or transmit.

Meanwhile waveShareTest 3 hack to bring in _sheet stuff on that analog data
Demo at 1pm, so maybe not.

Only got a bit done. Demo went very well.
Joe said to bill them for new AD board and another Pi3B+ (have on hand so easy to do.)

Needed to show writing to file (CSV) so I found couple ways
- direct via Numpy
  - numpy.savetxt("foo.csv", array, delimiter=",")
  - https://stackoverflow.com/questions/6081008/dump-a-numpy-array-into-a-csv-file
- using the CSV module
  - https://docs.python.org/3.4/library/csv.html
I used the first method in a mod to one of the UnitTestDemo functions

The OLED board flaked out for the demo. Might be a connector issue as unplugging and replugging made it work, for a short bit. Perhaps redo the I2C wiring to use qwiic ? That would allow easy addtion of more A/D or other modules

Noted the actual phase 1 calls for 16 channels of a/d but current board only as 8. We could easily add more 16 bit via i2c but it wont be possible to add more via the SPI cards

July 4th 2019
Phase 2 begins!!

Optimal Control Kalman Filters for sensor data stream
https://www.youtube.com/watch?v=gFeTkB8VHpw
moving average filter
Kalman filter https://github.com/lblackhall/pyconau2016
Hmm Python Logging! Log info, warning, error, etc
   https://www.youtube.com/watch?v=DxZ5WEo4hvU&list=PLs4CJRBY5F1KrUr7z_2mur2QdAKXyh-k3&index=13&t=0s

9 July
Daemons and Json and Linux Appliance
Setting up our MODAC daemon and client architecture
use Json to send data/cmds tween daemon and UI, logger, etc

10 July
looking back in bookmarks (incl Anouk python/pizero) find a bunch about message passing, queues, single and multi-threaded/processor and distributed messages

Our system will have local messaging w/in same Pi for
1. Deal with GPIO/I2C/SPI
  1. sensors (AD, environment, distance, etc)
  2. effectors (relays, DA, motors, servos, etc)
2. UI on small OLED
3. UI on touch-display
4. Comm to PC

NextGen Nano Message looks like good candidate. This article calls it spirtual successor to 0MQ ZeroMQ – no central server message queing.
https://pypi.org/project/pynng/
This one pypubsub seems like a decent message queuer for single process
https://libraries.io/pypi/PyPubSub

Found other bookmarks etc on general threading and python best libraries etc
also found thermocouple_reference module to install via pip
https://pypi.org/project/thermocouples_reference/

Transport Layer Security – TLS … optional in nng perhaps
we are ignoring security at this point but need to consider it down the line
dont want to be in a JPL-Hacked-Via-Rpi type headline

ok, so need a process that reads all the Inputs, packs em up in JSON and sends out pub/Sub
Then processes that subscribe and receive messages → Logger, UI
Or perhaps a Pair1(polyamorous=True) would be better?
Pair1 is bi-directional.
Or we set up a controller port that listens for requests, along side the Pub/Sub port?
One control in (signed requests by clients), and Publish port out?
Logging should be separate out port.

MODAC i/o Service (Mios) is the GPIO controller service.
- Configured by argparse, config file and runtime commands
- Controlls all reads/writes to GPIO Channels
- Channels are (device (+subdevice ids), config data, filters, direction, currValue
- Channels Published via NNG-JSON messages (secure? encrypted? TSL?)
- Control Channel via NNG receiver (secure, signed?)
- Direct python logger to SD file, plus NNG logger
  - common logger for all libraries in Mios!!
- GPIO: direct, i2c, spi, console serial(?)
  - Big Red Button – E-shutdown,
    - separate from panic button = All Power Shutoff
    - does orderly shutdown of GPIO ports
    - logs to log files, Informs UI
    - orderly shutdown of net services and OS

MODAC Logger Service: runs on either/both rPi and PC
- one or multiple log channels?
- listens/receives NNG log messages, writes to permanent storage

MODAC Process Scheduler
- runs PID control using subscriptions/nng cmds with MioS
- logs to SD and Logger
- has own config – argparse, file, runtime
- extensible PIDs via python script
- schedules from config files and cmd msgs
- takes cmds from UI streams

MODAC UI – rPi and PC
- as common as possible for primary Control UI
- hierarchy of active controls
  - front panel UI (buttons?) has top priority
  - Local GUI TouchDisplay has 2nd priority
  - Remote UI is 3rd priority

JSON samples:
{
“MODAC_MsgType”: “MultiChannel”,
“timestamp”: “datetimestring”,
“channels” : [
{
“chanId”: ‘AD0’
“dataType”: degC
“value”: 40.3
},
{
“chanId”: ‘AD1’
“dataType”: degC
“value”: 40.3
},
{
“chanId”: ‘AD2’
“dataType”: degC
“value”: 40.3
},
]
}

July 12 – forking this document onto MODAC Pi filesystem as MODAC Notes2.odt

created MODAC_Config folder to experiment with various configuration files
start with MODAC_Pins → MODAC_GPIO.ods → .csv → read into python and see what it looks like using
csv DictReader() That creates rows with column names per first line of file

GPIO_Config0.py in MODAC_Config folder explores ways to read csv into python and then out as json

Physical Mounting/Case

Found and bookmarked (on mac) a laser cut piB+ case designed for expansion… needs adaptation for ours
with added side area for out-board connections (AD/DA/DigitalIO)

BME280 needs to be located near the cold junction interface for K-type thermocouples
aka adjecent the T-amp board.

Also need physical board space for power buses/distribution bars
5vdc, 12vdc

Software Architecture
MODAC_io_server is core main tool. It controls access to the physical Pi hardware (mostly).
GPIO Configuration tested from csv and json
Logging startup shell written
InitLogging
InitHardware
InitDataSystem
InitEventSystem
EventLoop
read & dispatch messages (callbacks, sync and async)
(sync control config structures)
collect all input data
send scheduled gpio outputs
send messages (logging, pub/sub, etc)

Could have a highly configurable system of Channels, Devices, Messages
Or a simple initial hard coded with known devices etc
Latter lets us get the event and message system built
while working out the better ways with configurable data

UI hardware (OLED, HDMI/Mouse, etc) is by separate processes that have own config and shell. They will share some hardware (I2C bus and addresses). Hardcode that for now, but it can be in our Config Files
Hmm an I2C device registraion table/config file?
Address, shortName, longName, description, config data, handler routines

If nothing else, these tables would be good for our project documentation

13July evening
modac_OutputDevice.py built to abstract Relay and other Digital Out devices
figured out logging and try/catch a bit for error handling on array indicies
got its unitTest main() working… maybe look into Python’s UnitTest library sometime soon

sync’d with github
going on to next round with BME280 integration
and the F!@#*#& wires are screwed up again.
The big black JST pins keep popping out.
Can rewire so it goes to a qwiic connector and we have that for now and future

so break the soldering gear back out of storage box

Ok it works nicely now. Probably do similar for OLED soon.
Added UnitTests/03_BME280only.py
as raw adafruit bme280 test
modac_BME280 is now our wrapper on BME280, for integration into ioServer
   NOTE: we are NOT using the adafruit bme circuit python stuff

ok rough integration
but why does log file not have all the info level stuff
what happened to output?

15 July
* what happened to logging output when go into other modules?!!
* start on event loop and Channel Data

digging a bit into pynng and trio for sockets and async stuff
how do these communicate, work with GUI main loops ?

I can see making my own main loop in the io_Server
but the first client will be a text printer to its console
those should be fine without async I think

but how to get the matplotlib GUI back?

Logging was broke because modac_argparse callled logging
which initialized things wrong.
Move argparse to after logging

16 July
rebuilt AD preamp board to support 4 lines back to ADS board, connected 3 ktype
integrated k-type into reading/processing of main event loop (stub) of io-server
io Server now does something useful in creating input data log as data & json
what is better way for this?

How to do Channel Data and comms with other processes
can pynng work with gui loops?
Glib (Gnome lib) includes gtk_idle_add() to add a callback function when GTK main loop is idle long enough that its priority happens (priority=LEVEL parameter)
also gtk_timeout_add() adds callback function when timeout happens, returning true resets the timeout/call while false removes the timeout/callback
PyGObject may be better way to access Glib – see wiki.gnome.org/Projects/PyGObject/Threading

what about using QT framework? Should we explore that ? Nah, continue on ahead with GTK as known tool

Power fluxuation!
Yellow Lightning Bolt shows up in upper right of screen
this means the Pi is Under Voltage

wtf – i’m running it on a 5v 10A supply!
Ok so much of it is actually getting powered from the Pi’s regulated 5V (I think?)
we have two boards that draw off the Pi’s power stack
perhaps it is overloading the 3.3v side (regulated on Pi)

Ahh maybe its the 5v draw of the relay module, which is presently wired to the 5v tap on the proto-board
switch it to the external 5v bus. – wire direct?

Drat… that didnt solve the problem.
Still have Yellow Lightning Bolt… it goes off sometimes as I type. Weird

17July
 started network testing with pyNNG
really need to build up classes and stop using global !!

created relayModuleOff.py which should be on boot as the board seems to come up with relays ON

ok… refactoring time.
Moving io data stuff to modac package
need to packge and install the waveshare stuff so it runs proper
or make it part of modac

still having low power issues with pi.
Reading Adafruit on the ‘powered’ hub, seems you need to open the hub, cut the 5v to usb line
and then provide 5vdc in on the side plug – from the 5vdc main
cut line, cut power plug and wired to bus
STILL have power issue!
Is it the waveshield board?
Tracked down to (I think) an inadequately small wires in the USB-C from power bus to Pi.
Replaced with CanaKit supplied pi 2.5a supply direct into pi and it works fine.
Ordered some usb-c 3.1 power cables that we can hack into the power bus

Finished large refactoring into modac sub package w/waveshare as side piece
took some twiddling but its better now with lots of cleanup to do
modac_ioserver2 runs the nng network pub/sub – sorta. It seems to lose some messages but that may be error in the test code.

Need to build a Modac_Logger server that listens to the pub/sub channel and logs all traffic, esp allData messages
Then build control channel in io-server
and control channel tester routine, then GTK app listener/controller

21 July
retired server2 as nng one process pub-sub via socket
created netLogger and revised server to be a working pair of processes
mods to moNetwork to clean it up
test worked well, at least for a basic functional check

next need to work on how to get Subscription to work.
Explore by going back to a single process?
Perhaps explore using py-pubsub intraProcess pub/sub
which might make it work ok with network version
Docs say pub/sub works ok with netMQ or something, so maybe with nng or switch?

Ok got the pub/sub running with tester.
TestSubscriber does the basic read and log… could convert easy to moLogger()

24 July
On to the Control side… how to send BinaryOutput on/off cmds from network clients?
What type of nng would allow multiple senders with one listener port?
And what security is on that port – recommending we add our own layer
perhaps encrypt/decrypt message contentts

later we will rework moNetwork to use “modac.local” and mDNS to resolve that to ipAddress for modac server
clients dont need fixed ip or name
then will figure out how to run GTK and logger etc on Windoze
or perhaps ZeroTier? https://zerotier.com/

pub/sub nng Pair1 polyamorous=True seems to be the socket level
our open calls would use that
subscribe() call returns the subscriber as well as stuffnig it into array so calling level can use that
allows for multiple subscribers in process, but at present we only have one in a process
could perhaps combine upper logic into one App for PC

setup startModac.sh to run the server as process
add to .bashrc

alias startModac=/home/pi/MODAC_Dev/startModac.sh

so this becomes command line tool, easy to start via sh/ssh

Looked into Pair1 and it seems to be thing to use for the Server <= cmds from <= Client stuff
Refined moNetwork to use startClient() startServer() as these will be different.
Also clientReceive() and serverRecieve() are going to be different
(not sure of spelling)
dispatch should be basically the same once down to topic msg pair
and this could be recusive … split a msg, decrypt data, extract new topic/data pair, dispatch
no. thats a security hole – restricted topics and open topics should NOT run thru same Dispatch code
other than first level dispatch of serverCmds (topic=’modac’), which would dispatch to the serverDecryptAndDispatch()

25 July
Talked with Joe this week and got Leica Laser Distance sensor to integrate
Phase 2 requires demonstrating on Kiln – revised SOW aims to bring explicitly in line with other 2 docs/versions
Added back the AD16 – ADS1115 16bit a/d converter using i2c which caused some refactoring
have not fully integrated it but it now works sending via server and receiving via client

Leica integration has not been started. Ian’s test code uses external process running “gatttool” cmd line tool to talk bluetooth with it. May do this or may use blueZ library more directly. Ian code may be faster to code but take a while to run each Update(). Not too worried about that now, maybe P3 time

code to integrate AD16 was added while only part way into the Client Cmd refactoring
I got it to work enough = had to refactor a few times and get the right stuff for key-Divider-body packaging
especially with the modacEncrypt/Decrypt layer of encryption stuff. Not sure yet how best to add that.
For now using the hexlify and unhexlify method, which doesnt really encrypt but simply converts to hex string

Next up in getting Cmd side working
Need to refactor the moNetwork into moNetwork, moClient, moServer
with Network holding the common stuff and Client/Server providing their separate functions
in particular the ServerRecieve/Dispatch needs to import moHardware and BinaryOutput

Talked with Joe about adding PWM i2c board for servo and better analog out (incl adding support for D/A of the AD hat)
those will both be POST-Proof of Concept phase

Noting that Visual Studio Code is available for Raspberry Pi, according to several web sites etc
not sure how easy it is to get running but that would be VERY preferrable to Thony as we get into more elaborate/advanced development. Refactoring is becoming harder and harder.
https://pimylifeup.com/raspberry-pi-visual-studio-code/
https://visualgdb.com/tutorials/raspberry/
https://github.com/Microsoft/vscode
https://github.com/headmelted/codebuilds
works but need to downgrade version to avoid blank box window, per comments in that first article
sudo apt-get install code-oss=1.29.0-1539702286
sudo apt-mark hold code-oss
july 27
Now trying refactoring
well its slow and cant figure how to simply run py code, so back to Thony
Client/server seem to be working with new moNetwork/moClient/moServer
testClientSender turns binaryOut on/off on 2sec
but it seems to have issues starting.

But works enough for now.
On to Leica Disto D1 laser distance sensor
Ian code uses gatttool and pexpect to get data via other process/pipe
also includes a temp sensor we arent using so skip that
hcitool gives address of Leica as
  D3:9D:70:68:8B:F2 DISTO 84312758

ok readLeica works IF you turn on device first.
Next integrate that into system moHardware, etc
note pyGatt is a python alterantive to using pexpect
   https://pypi.org/project/pygatt/

This page gives juicy details on the Generic Attribute Profile of BLE
    http://dev.ti.com/tirex/content/simplelink_cc2640r2_sdk_1_40_00_45/docs/blestack/ble_user_guide/html/ble-stack-3.x/gatt.html
Adafruit also has a decent but too slim intro:
    https://learn.adafruit.com/introduction-to-bluetooth-low-energy/gatt
Here is the official description page for GATT characteristics
    https://www.bluetooth.com/specifications/gatt/characteristics/

and the pexpect version works!!
will need to clean up logging and print statements soon but looks good for moving on to GUI!!!
Aug 1 2019
Gui system works!
Some oddities, like latency from click to feedback (cmd send, rcv, data send, receive) and Leica power down
Used gattool for leica as it was proven method, but maybe not.
Needs extended testing there

GUI – using GTK + Glade + code built & code backed with the moData moNetwork seems to work well
not a lot of good info on how to build reusable ones but now that I’ve got a shell, we can make more apps easier
and experiment with GUI designs with out major changes underneath

Build a Panel with Python + Glade,
Unit Test Panel with single loader Main App
Common GUI tool loads panels into multi-page NoteBook container

Aug 3
show and tell with Joe went well on friday 2Aug
modac turned kiln on/off from gui
relay 6 jitters in sync with read/send – turns out I misread all the gpio=pin-piEZ pins and need to move relays 6 and 7
because current pns are used by A/D D/A board for Chip Select!!
(gpio 8, 7, pin 24, 26) move to gpio 23, 25 (pins 16, 22)
so where are those on the EZ connect? Inside. Need longer wires
see Modac config MODAC_GPIO2.ods

Aug 7
whole lotta work done… see paper notebook and git log

almost all working now.
Last step for P2 is to build up a PID scheduler
found two very nice ones on github for rPi and they both seem to use same base code
   https://github.com/apollo-ng/picoReflow
   https://github.com/jbruce12000/kiln-controller

both are pretty simple oven/ovenWatcher/webserver
oven – runs hardware, uses Profile ([time,temp], [t,v] …]) for schedule, on demand gives ovenStatus
ovenWatcher – periodically gets oven status and sends to all registered watchers as json data
webserver – registers web clients to get updates
somewhere there is graphing and editing of the profiles

Use oven as template for our own Kiln
- lives in server, publishes kilnStatus messages, Pair1 receives KilnCmds
- defines K types and Relays for thermo and heaters
- reads a Schedule (profile)
- async loop at KilnRate to compute PID and set Heaters, etc
- comment for where it might use Distance, etc
- has Safety shutdown – if kilnTemps over threshold, shutdown and Alarm

….
13 August Met with Joe et al at IFA lab to show phase 2 working
time was short and there were failures – hard and soft – but it worked well enough to bill
Lots of design documentation was done in paper journal (grey cover, quad ruled paper)
so need to reference/scan those notes.

The move to Async and multi-threaded design removed some major issues, at the expense of major step in complexity of system. Client-Server model using pyNNG works nicely – some glitches. But good enough
Trio seems to be good foundation for threading, although there needs to be ways to manage it – especially for configuration and canceling tasks. Getting good checkpoints is important… and a source of deadlocks and speed issues.

Need to investigate Sempahores etc under Trio, as well as Nursery Management – for handling failure and recovery modes.

See other docs for some notes---
Setup MODAC SD Images.odt
MODAC P3 ToDo.rtf
MODAC SOW v4a.rtf
Sept 6
adding VNC so remote can see desktop on linux

sudo apt-get install -y realvnc-vnc-server realvnc-vnc-viewer dnsmasq hostapd

need:
* dns name or config’d ip address
* start vnc server and ssh access via net porT
name = modacServer
should be modacServer.local

on pc realvnc.com/en/connect/download/viewer
  download and execute
or copy to/from sd card

start> vncserver
pi@modacServer:~ $ vncserver
VNC(R) Server 6.4.1 (r40826) ARMv6 (Mar 13 2019 16:35:06)
Copyright (C) 2002-2019 RealVNC Ltd.
RealVNC and VNC are trademarks of RealVNC Ltd and are protected by trademark
registrations and/or pending trademark applications in the European Union,
United States of America and other jurisdictions.
Protected by UK patent 2481870; US patent 8760366; EU patent 2652951.
See https://www.realvnc.com for information on VNC.
For third party acknowledgements see:
https://www.realvnc.com/docs/6/foss.html
OS: Raspbian GNU/Linux 9, Linux 4.19.57, armv7l

Generating private key... done
On some distributions (in particular Red Hat), you may get a better experience
by running vncserver-virtual in conjunction with the system Xorg server, rather
than the old version built-in to Xvnc. More desktop environments and
applications will likely be compatible. For more information on this alternative
implementation, please see: https://www.realvnc.com/doclink/kb-546

Running applications in /etc/vnc/xstartup

VNC Server catchphrase: "Paprika Bermuda basic. Maze Ringo Gloria."
        signature: 7b-fb-3f-0a-7c-11-12-31

Log file is /home/pi/.vnc/modacServer:1.log
New desktop is modacServer:1 (192.168.1.147:1)
pi@modacServer:~ $
–
on pc find the icon and use that ipaddress:1

user pi
pwd modac

and we in…
oh that was hard

using ssh?
Need to turn it on
https://www.raspberrypistarterkits.com/how-to/enable-ssh-raspberry-pi/

 run raspi-config
in interface options enable ssh

or using system Preferences
Interfaces, enable ssh and vnc

----
27Jan2020
calibration tests were inconclusive.
There is significant noise on the thermocouple amp lines.
There were a whole series of Calibration runs in Nov/Dec on desktop (no kiln)
running in ice water, boiling water, etc to get set points and scale
Then in late dec (jan?) we ran it in kiln with one thermocouple

shifted over in January to building the case
APC rack mount from IfA junk piles serves as nice enclosure.
It has openings in front and back, plus AC power plugs.
A wood panel was laser cut with mounting holes for board-box and pi, relay module, 5v pwr/gnd strips
front panel has two openings and a cardboard front was created.
On left front is opening for the 7” LCD Touch Display. On right is smaller openting that holds the OLED, ethernet, and usb/hdmi jacks.
LCD mounting stack was created for internal bezel/pad, lcd panel, cardboard pad, cardboard mount panel, driver board
unfortunately it was cut upside down wrt front opening and location of connectors on driver board
Will need to flip and recut both stack and front panel

back panel has two usable openings. Smaller one gets the thermocouple amp connector. Taller one in center gets
- relay connection to heaters
- jacks for 3 controlled power strips
- holes for 5vdc wires (no jacks, so cable runs inside to wire to 5v strips)

Unit set up at IfA for more kiln testing
Note: LCD touch-display is not installed. OLED is not wired

OLED: Adafruit had changed the design and new model comes with i2c qwiic connectors. Since we are building 2 of these, get 2 of the new ones

Need good cable jacks. The thermocouple cable may need to be turned into twisted pair

Alternatively, there is a new i2c thermocouple board with qwiic connectors. 3 of these would remove calibration concerns for our AD.
Could also use i2c-RJ45-i2c for better shielded comms.

Looking to the GUI control -
It is VERY slow in responding – in feedback that a button has clicked, and latency for a change to register (round trip: cmd click – cmd send – change reported)
perhaps due to running both server and client on same Pi

So porting Client to PC (or other machine)
- need fixed ip addresses 192.168.23.23 for server 192.168.23.x for clients
- linux should be easy
  - ubuntu (dual boot) desktop
  - other pi
- require Windows system per contract
  - winPy for building distributable version
  - how build for windows – installing required python packages?
- Touch Designer
  - very nice graphic interfaces
  - not sure about Plotting widgets
  - python based so data in should be fairly simple pyNNG link

14 February

QWIC
All Qwiic cables have the following color scheme and arrangement:

Black = GND
Red = 3.3V
Blue = SDA
Yellow = SCL

SDA = pin 3 ; on EZ-Connect its 3rd = white wire on MIOAT pi
SCL = pin 5 ; on EZ-Connect its 4th = green wire on MIOAT pi

python conversion of MCP9600 code is tad complex

---
20 feb
for 18Feb test, put the BME280 environment sensor in the TC amp box, using i2c differential extenders from Sparkfun (uses cat5/rj45)
gives temp in the box, showing temp going up from 23 to 34C in first hour
but this isnt enough to account for discrepancy

re-evaluate the calculations
our AD→ C is
adScaled0-5 (read AD, scale24 bits to 0-5V)
v = (adV-offset)/ampGain = adV/ampGain – offset’ = adV/aG
mV = v*1000.0
C = kType.inverse(mV, ambTemp)

expected: (kissC→aD)
mv = kType.emf_mVC(kissC,ampTemp)
v = mv/1000
aDv = v *amGain
ampGain = aD/v = aDv/mvFromC/1000 = adRead/kType(C,ambTemp)/1000